## Slide 1
​
GAITPARITY
Side-aware representations
for balance-relevant gait analysis
A scientific story from dynamic stability to parity-aware JEPA and independent-force validation
Motivation • measurement • architecture • training • experiments • current evidence
Scientific research presentation • 2026
Notes: Open with the measurement problem: the goal is not symmetry for its own sake, but a representation that preserves the mechanics needed for credible balance assessment.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md

## Slide 2
MOTIVATION
Walking is controlled instability, step after step
GaitParity
02
During gait, the body’s center of mass is outside the base of support for much of the cycle.
•
Each step relocates the base of support to redirect the moving body.
•
Foot placement, ankle moments, and push-off regulate forward and mediolateral stability.
•
Balance failure can emerge dynamically even when quiet standing looks adequate.
​
Dynamic balance is the relation between body state, foot placement, and the forces that redirect motion.
​
STATE → ACTION → STABILITY
Winter, 1995 • Bruijn & van Dieën, 2018 • Ribeiro et al., 2024 figure (CC BY)
Notes: Walking is not static posture repeated. It is continuous regulation of a moving center of mass, so a useful gait representation should preserve the mechanics that distinguish how each side contributes to that regulation.
[Sources]
- https://doi.org/10.1016/0966-6362(96)82849-9
- https://pmc.ncbi.nlm.nih.gov/articles/PMC6030625/
- https://pmc.ncbi.nlm.nih.gov/articles/PMC10883149/
- https://cdn.ncbi.nlm.nih.gov/pmc/blobs/5ea6/10883149/3bfb8ca47aff/peerj-12-16919-g003.jpg

## Slide 3
MOTIVATION
Falls make gait a clinically consequential signal
GaitParity
03
​
1 in 4
U.S. adults ≥65 report falling each year
Falls are the leading cause of injury in this age group.
​
​
Prospective evidence
Maki followed 75 older adults for one year: stride-to-stride variability—especially speed variability—predicted future falls more clearly than several slower, more cautious gait adaptations.
​
​
Independent signal
In 597 community-dwelling elders, quantitative gait domains predicted incident falls over a mean 20-month follow-up, beyond several clinical risk factors and gait/balance tests.
​
The assessment gap
Instrumented walkways and force plates reveal mechanics, but they are episodic and scarce. Video skeletons are scalable, but ordinary representations may discard laterality or learn camera shortcuts.
​
Scientific boundary
Gait markers can inform risk assessment; they are not themselves a diagnosis or a causal proof of falling.
CDC, 2026 • Maki, 1997 • Verghese et al., 2009
Notes: The motivation is not that one gait metric can diagnose falls. It is that prospectively observed gait variability and rhythm contain risk-relevant information, motivating scalable measurement of richer gait mechanics.
[Sources]
- https://www.cdc.gov/falls/data-research/index.html
- https://pubmed.ncbi.nlm.nih.gov/9063277/
- https://pmc.ncbi.nlm.nih.gov/articles/PMC2709543/

## Slide 4
MOTIVATION
The missing link is side-specific control
GaitParity
04
​
​
Neurologic injury
Unequal motor capacity and timing
→
​
​
Side-specific force
Paretic vs nonparetic propulsion
→
​
​
Compensation
Speed may improve without paretic recovery
→
​
​
Balance reserve
Adaptability may fail under challenge
​
Why propulsion is the bridge
•
Fore–aft ground-reaction force measures how each limb contributes to forward progression.
•
Post-stroke training can shift the contribution of paretic and nonparetic propulsion—even when walking speed alone hides the mechanism.
​
What GaitParity will test
Can video-derived skeleton motion preserve enough signed information to estimate an independent right-versus-left force target for a person the model has never seen?
Not yet: prospective fall prediction.
Hsiao et al., 2016 • Bowden/Kautz propulsion framework • Lodha et al., 2025
Notes: Signed propulsion is used because it is a side-specific mechanical measurement from an independent instrument. The talk deliberately stops short of claiming that propulsion asymmetry alone predicts falls.
[Sources]
- https://pubmed.ncbi.nlm.nih.gov/26721869/
- https://www.ahajournals.org/doi/pdf/10.1161/str.37.2.619
- https://pubmed.ncbi.nlm.nih.gov/40250067/
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY.md

## Slide 5
QUESTION
Scientific hypothesis: geometry can reduce the label burden
GaitParity
05
​
A parity-aware encoder should make signed propulsion easier to recover from few labelled participants than output repair or an equally capable unconstrained paired model.
​
​
P1 • Exact geometry
Every claimed encoder layer commutes with the left–right branch swap.
​
​
P2 • Informative laterality
The odd channel varies across people and retains healthy effective rank.
​
​
P3 • Useful mechanics
Held-out participant force MAE improves versus both decisive controls.
​
​
P4 • Robust measurement
Benefit persists across label budgets, views, and realistic corruption.
Claims are cumulative: geometry → information → prediction → balance-relevant validation.
Notes: Present the hypothesis as a chain. Exact geometry is necessary but does not establish usefulness; independent force prediction is the key utility test.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md

## Slide 6
MEASUREMENT
One gait cycle, two instruments, one signed target
GaitParity
06
​
Skeleton input
x ∈ ℝ⁶⁴×¹¹×³
2.13 s at 30 Hz • core-11 joints • forward/up/side axes • visibility mask carried through
​
Independent force target
y = ln(Jᴿ / Jᴸ)
J is the positive fore–aft ground-reaction impulse during stance. The log ratio is scale-free, centered at zero, and exactly sign-flipping under side exchange.
​
Critical separation
The model sees motion; the target comes from sensors in the floor. Geometry cannot manufacture the answer.
Notes: This is the decisive measurement design. Coordinate-derived asymmetry is acceptable for audits, but the primary study uses force so the input and target are not the same signal in different notation.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/what-we-predict-propulsion.svg

## Slide 7
GEOMETRY
Anatomical reflection is not a camera move
GaitParity
07
​
​
Operator M
Negate the mediolateral coordinate; swap all five bilateral core-11 pairs; swap visibility/confidence; keep time, forward, and vertical unchanged.
​
M(Mx) = x
Involution unit test
​
s(Mx) = −s(x)
Odd signed target • camera view should stay ≈ invariant
Mirror swaps anatomy; camera motion changes projection, visibility, and estimation error.
Notes: Emphasize the visibility-mask swap. Reflecting coordinates without masks creates impossible bodies and lets the model detect the synthetic operation instead of anatomy.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/reflection-operator-steps.svg

## Slide 8
METHODOLOGY
JEPA predicts missing motion in representation space
GaitParity
08
​
1
Tokenize
64 frames → 16 four-frame patches × 11 joints
​
2
Mask
Hide valid spatiotemporal tokens; Stage 2 example uses 60%
​
3
Predict
Student context + predictor estimate hidden teacher latents
​
4
Update
Teacher encoder follows the student by exponential moving average
​
5
Audit
Variance, covariance rank, cosine similarity, and odd energy
​
No force labels, diagnosis labels, affected-side labels, or BABEL categories enter the pretraining batch.
Notes: The objective is self-supervised: the model predicts a teacher representation of hidden motion, not the missing coordinates and not a clinical label.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/05-two-stage-amass-training-overview.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/what-a-jepa-predicts.svg
- https://doi.org/10.1007/978-3-031-73411-3_21
- https://arxiv.org/abs/2301.08243

## Slide 9
ARCHITECTURE
GaitParity lifts each walk into a two-element reflection orbit
GaitParity
09
​
H⁰(x) = [φ(x), φ(Mx)]
Mirroring x swaps the two branches—nothing more.
​
Fₗ(SH) = S Fₗ(H)
Swap then process = process then swap, at every layer.
•
Symmetric cross-branch interaction makes the paired interior meaningful.
•
Masks, dropout, normalization, positional encoding, and EMA teacher updates must preserve the swap action.
​
Naming rule
If a claimed layer fails the commutation test, the system is parity-regularized—not equivariant.
Notes: The two-element group C2 makes the construction tractable. The scientific claim rests on layerwise numerical commutation tests, not on the architecture diagram.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/long-term/commutation-square.svg
- https://proceedings.mlr.press/v48/cohenc16.html

## Slide 10
ARCHITECTURE
Exact oddness is easy; useful odd information is hard
GaitParity
10
​
h_even = (h_orig + h_mirr) / 2
h_odd = (h_orig − h_mirr) / 2
​
​
Control 1 • odd_output
Wrap any scalar predictor as [f(x) − f(Mx)]/2. It guarantees the final sign rule with no equivariant encoder.
​
​
Control 2 • paired control
Same two branches, cross-branch interaction, masks, compute, seeds, and outer odd wrapper—without swap-consistent tying.
​
Representation health gate
Odd-channel variance + covariance effective rank + energy by participant + masked prediction quality. Perfect mirror error with a zero channel is an invalid success.
Notes: The co-primary comparisons are intentionally difficult. The equivariant encoder must beat both cheap output repair and an equally capable paired model without equivariant tying.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/long-term/output-vs-encoder.svg
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/long-term/collapse-trap.svg

## Slide 11
TRAINING
Training is a two-stage, label-free curriculum
GaitParity
11
​
​
Stage 1 • broad AMASS
Convert participant-disjoint motion to core-11, index 64-frame windows, and train the three matched JEPA variants. Current inventory: 10,941 sequences / 308 candidate subjects; production identity audit and trainer remain to complete.
​
​
Traceable handoff
Load student, teacher, predictor, projector, centering state, and model buffers. Record the exact parent hash. Reset optimizer, learning-rate schedule, step counter, and early-stopping state.
​
​
Stage 2 • BABEL walking
Continue the same masked objective on clean walking intervals cut from the same AMASS universe. BABEL changes which windows are sampled; categories never enter the batch. Freeze the encoder before clinical readouts.
→
→
​
64 × 11 × 3
Frozen window and skeleton contract
​
4 frames
Temporal patch size → 16 time patches
​
60%
Stage 2 example mask fraction
​
5 × 10⁻⁵
Stage 2 example AdamW learning rate
​
Protocol status: the production AMASS converter, BABEL manifest builder, and full trainer are planned interfaces—not completed experiments.
Notes: Treat the numeric configuration as a proposed starting point frozen through nonclinical development, not as validated hyperparameters. Preserve the implementation-status boundary visibly.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/05-two-stage-amass-training-overview.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/06-stage-1-broad-amass-pretraining.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/07-stage-2-walking-focused-continuation.md

## Slide 12
TRAINING
Architecture comparisons must isolate the mechanism
GaitParity
12
Held constant | Why it matters
Participants, source motions, window order | Prevents one variant from receiving easier movement data
Original/mirror exposure + token masks | Separates architecture from augmentation or masking luck
Embedding width, effective depth, parameters | Prevents capacity from masquerading as parity
Optimizer, schedule, updates, stopping | Prevents extra training from becoming the result
Teacher update, regularization, augmentation | Keeps the JEPA objective comparable
Paired seeds: 7 vs 7, 17 vs 17, 29 vs 29 | Measures architecture rather than best-of-seed luck
​
​
Exposure-matched
Same original windows, mirrored windows, masked tokens, and update count. GPU cost may differ.
​
​
Compute-matched
Same prespecified compute allowance. Windows or updates may differ. Report FLOPs, throughput, wall time, memory, and inference cost.
​
Planned family
3 variants × 3 paired seeds × 2 stages × 2 matching regimes = 36 runs
Notes: One comparison cannot match data exposure and GPU cost simultaneously. The deck therefore names both regimes and never implies a match that was not achieved.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/05-two-stage-amass-training-overview.md

## Slide 13
EXPERIMENTS
Each dataset answers one question—and no more
GaitParity
13
Dataset | Scientific role | Hard claim limit
GAVD | Code + geometry audit | Transductive; no participant IDs; coordinate-derived target
AMASS | Nonclinical pretraining | No clinical or fall-risk claim
MoVi | Calibrated real-view sensitivity | Geometry/robustness only
Stroke cohort | Primary signed force test | Utility on held-out participants
Parkinson cohort | Locked replication | Replication, not zero-shot transfer
Future falls cohort | Prospective outcome validation | Required before a fall-risk claim
​
Only independent, participant-held-out force can establish utility.
Notes: The ladder prevents a common narrative error: using exact geometry or a transductive audit to imply clinical utility.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/research-ladder.svg
- https://doi.org/10.1038/s41597-023-02767-y
- https://doi.org/10.1109/ICCV.2019.00553
- https://doi.org/10.1371/journal.pone.0253157

## Slide 14
EXPERIMENTS
Generalization is tested on people—not clips
GaitParity
14
​
​
Nested participant split
Outer fold holds out one participant group. Inner grouped folds tune the readout. The outer person never influences preprocessing, representation selection, or hyperparameters.
​
​
Label-efficiency ladder
Use nested 4, 8, 16, and all-participant training prefixes; repeat fixed side/severity-stratified orderings and average repeats within participant.
​
​
One independent unit
Score original and synthetic mirror equally, average to one participant-orbit loss, then resample whole participants for uncertainty.
​
Force gate: ≥30 eligible stroke participants after all screens, with ≥4 usable contacts per side for repeatability.
Notes: Random clip splits are unacceptable because clips from the same person and capture setting can leak across evaluation. The inferential unit is the participant.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/participant-safe-split.svg

## Slide 15
EXPERIMENTS
Success is predeclared as a chain of evidence
GaitParity
15
​
​
G1 • Exact geometry
Layerwise swap residuals in train/eval mode; output oddness for every signed model.
​
​
G2 • Alive representation
Variance, effective rank, cosine similarity, even/odd energy, JEPA prediction quality.
​
​
G3 • Predictive signal
Participant-orbit force MAE primary; NMAE, R², CCC, sign accuracy, calibration secondary.
​
​
G4 • Robust utility
Label-budget AULC, real-view drift, coordinate/missingness/temporal corruption, schema reduction.
​
Tier 5 decision
At the full label budget, equivariant_encoder must lower participant-orbit force MAE versus both odd_output and paired_unconstrained, using simultaneous 97.5% intervals and a reliability-based δMAE threshold.
Notes: Do not compress the result to one conjunctive pass/fail. Report the highest supported tier and the specific gate that failed.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md

## Slide 16
CURRENT EVIDENCE
First result: self-supervised training learns nontrivial motion
GaitParity
16
What this supports
•
Optimization loss moves in the expected direction.
•
Feature variation persists; the encoder is not obviously constant.
•
Folder-label separation remains confounded by source, camera, and exposure.
Exact notebook outputs • development collection • not unseen-person or force evidence
Notes: The first result is optimization competence, not disease understanding. State that boundary before discussing the classifier visualization.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notebooks/foundations/04_pretrain_sjepa_on_normal.ipynb
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notebooks/foundations/06_capstone_health_condition_classifiers.ipynb
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/01-foundations-notebooks-00-06.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/04-notebook-graph-guide.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/images/notebook-04-curriculum-diagnostics.png
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/images/notebook-06-all-sequence-confusion.png

## Slide 17
CURRENT EVIDENCE
Second result: the historical representation lacks a signed axis
GaitParity
17
Test | Saved result
Held-out-source decoding | R² = −0.068
Mirror slope | −0.34; target ≈ −1
Verdict | Informative null
Claim ceiling | Transductive audit
​
Why the null matters
This checkpoint + simple readout did not recover a useful signed direction. The result justifies a representation whose parity is explicit and testable.
Exact output from idea05_signed_laterality/01_probe.ipynb
Notes: Treat the null as a scientific result: it rules out the easiest story that the old representation already contained a clean signed gait direction.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notebooks/experiments/idea05_signed_laterality/01_probe.ipynb
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/02-current-direction-and-results.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/04-notebook-graph-guide.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/images/notebook-05a-signed-laterality-probe.png

## Slide 18
CURRENT EVIDENCE
Third result: the controlled audit detects broken geometry
GaitParity
18
​
0.0
Equivariant residual • worst checked
​
≈5.9
Unconstrained residual • audit power
​
96 / 18 / 394
Sequences / videos / windows • 3 seeds
Geometry is validated locally; force utility, unseen-person generalization, and fall-risk value remain unknown.
Notes: The unrestricted control is crucial: it proves that the audit can fail when the geometry is actually broken. This is feasibility, not utility.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notebooks/experiments/idea09_reflection_equivariance/05_gavd_audit.ipynb
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notebooks/experiments/idea09_reflection_equivariance/06_cpu_replication.ipynb
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/work/artifacts/gait_parity/real/gavd96-cpu-strong-v1/exposure/checkpoint_audit.json
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/work/artifacts/gait_parity/real/gavd96-cpu-strong-v1/exposure/checkpoint_geometry.csv
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/02-current-direction-and-results.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/04-notebook-graph-guide.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/tutorials/images/notebook-09f-full-gavd-audit.png

## Slide 19
FUTURE WORK
The decisive experiment moves from geometry to force
GaitParity
19
​
1
Audit force
Verify bilateral contacts, repeatability, and ≥30 eligible stroke participants.
​
2
Freeze encoders
Complete matched AMASS Stage 1 + BABEL walking Stage 2 checkpoints.
​
3
Run the primary test
Nested held-out stroke force prediction versus odd_output and paired_unconstrained.
​
4
Stress the measurement
MoVi real views, coordinate/missingness/temporal corruption, and reduced joint sets.
​
5
Extend the claim
Locked Parkinson replication; only then design prospective fall-outcome validation.
​
Stop rule: if equivariance does not beat both decisive controls on independent force, do not elevate it to a fall-risk model.
Notes: Future fall validation should ask whether force-informed, side-aware gait signatures add prospective information beyond established gait and balance measures—not assume that they will.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/images/label-efficiency.svg
- https://pubmed.ncbi.nlm.nih.gov/9063277/
- https://pmc.ncbi.nlm.nih.gov/articles/PMC2709543/

## Slide 20
​
CLOSING THESIS
GaitParity is not a fall detector.
It is the representation test required before side-aware video gait can become a credible balance measure.
Balance
needs side-specific mechanics
→
Parity
supplies predictable geometry
→
Independent force
decides whether it is useful
Geometry first. Force next. Falls only after prospective validation.
Notes: End on the scientific sequence. The contribution is credible only if the talk preserves the distinction between a geometrically correct representation, a useful biomechanical estimator, and a clinically validated fall-risk tool.
[Sources]
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/README_LONG_TERM.md
- /Users/theodoremui/dev/alexpose/experiments/sjepa/gavd6/notes/research/programs/gait_parity/METHODOLOGY_LONG_TERM.md